## Slide 1: CRESCO ENEA HPC clusters: a working example of a multifabric GPFS Spectrum Scale layout
Teacher: Annajiat Alim Rasel Written by: Nawroze Baizid Mohammed(20201108)

## Slide 2: ENEAGRID/CRESCO Infrastructure:
ENEAGRID/CRESCO Overview
Italian National Agency for New Technologies, Energy, and Sustainable Economic Development
Operates in energy, materials physics, life sciences, and climate studies
Infrastructure Highlights
Distributed across 6 sites with HPC CRESCO clusters
IBM Spectrum Scale (GPFS) as primary storage solution
Data Accessibility
GPFS manages data access, including WAN accessibility
Implemented GPFS multifabric for storage across clusters

## Slide 3
Cluster Details
CRESCO6: 1.4 Pflops, Intel Xeon X86_64 SkyLake CPU (Ranked 420th in TOP 500 Nov.2018)
CRESCO6 uses Intel Omni-Path (OPA) for interconnection (100 Gbps)
Previous clusters use InfiniBand QDR Truescale fabric (40 Gbps)
GPFS Multifabric Implementation
Implemented for storage efficiency across clusters

## Slide 4: Introduction:
CRESCO6 Introduction
Installed at ENEA Research Center of Portici since Oct. 2018
Significantly enhances ENEA's computational infrastructure, providing a 10x performance increase
Storage Infrastructure Evolution
Initial storage: DDN raid systems using Infiniband Qlogic Truescale
GPFS provided to HPC clusters CRESCO4/5 via the same fabric
Integration Challenge with CRESCO6
CRESCO6 introduced Omni-Path fabric by Intel
Integration challenge: How to access the same storage infrastructure with different fabrics

## Slide 5
Technical Focus
Describes the technical specifications and benchmarks of CRESCO6
Details the implementation of a multi-fabric layout to operate Infiniband and Omni-Path on a single GPFS cluster using shared storage systems

## Slide 6: CRESCO6 Technical Specifications:
System Configuration
HPC Composition: 434 nodes totaling 20,832 cores
Hardware Base: Lenovo ThinkSystem SD530 platform
Node Configuration: 2 Intel Xeon Platinum 8160 CPUs, 192 GB RAM per node
Networking Interface: Intel Omni-Path 100 Series Single-port PCIe 3.0 x16 HFA
Interconnect: Intel Omni-Path network with 21 Intel Edge switches (100 series, 48 ports each)
Network Details
Bandwidth: 100 GB/s
Latency: 100ns
Topology: 2 tier 2:1 no-blocking tapered fat-tree

## Slide 7
Cluster Performance
CRESCO4: 100 Tflops peak rate (Infiniband QDR network)
CRESCO5: 25 Tflops peak rate (Infiniband QDR network)
CRESCO6: 1.4 Pflops peak rate (Omni-Path network)
Special Nodes Section
Features: Large memory, accelerator CPUs (Intel Xeon PHI KNC, Nvidia GPU Tesla K40)
Network: Infiniband QDR network
Storage Systems
DDN Solutions: S2A9900, SFA7700/990 with Infiniband-based network
Filesystem: GPFS Spectrum Scale with 6 NSD nodes enabling parallel I/O

## Slide 8: CRESCO6 Benchmarks:
Deployment Phases
Initial Deployment (Early 2018):
  700 Tflops peak performance
  216 Skylake nodes
  Omni-Path network (1:1 no-blocking tapered fat-tree)
Second Phase:
  Doubled to 1.4 Pflops peak performance
  434 Skylake nodes
  Omni-Path network (2:1 no-blocking tapered fat-tree)
A. HPL Benchmark
Performance: Ranked 420th in TOP 500 Nov.2018 list
Configuration: 434 nodes, 2 MPI tasks per node
Results: Achieved around 72% efficiency, up to 1.012 Pflops

## Slide 9
B. Molecular Dynamic Simulations
Benchmark: Utilized ORAC6 MD code
Comparison: MARCONI A1 Broadwell CPU platform at CINECA
Simulation Details:
  REM Stage: CRESCO6 vs. MARCONI/A1
  FNE Stage: CRESCO6 vs. MARCONI/A1
Observations:
  CRESCO6's AVX512 vectorization enhanced performance
  Thread normalization essential for optimal performance
  CRESCO6 observed to be approximately 30% faster than MARCONI/A1 post-optimization

## Slide 10: Multifabric GPFS Layout:
Challenge Overview
Deployment Challenge: Integrating different fabric technologies into a unified infrastructure for CRESCO6 within the existing CRESCO data center
Objective: Enable seamless functioning of Infiniband QDR, Infiniband FDR, and Omni-Path fabrics with the Spectrum Scale GPFS
Hardware Components
Storage Systems: DDN Infiniband QDR/FDR/EDR
NSD Servers for GPFS:
  Configuration: 2U Lenovo ThinkSystem SR650, 96 GB RAM, 2 Intel Xeon Gold 5518 CPUs
  Network Interfaces: QLogic IBA7322 QDR Infiniband HCA, Mellanox MCX454A-FCAT DUAL FDR Infiniband HCA, Intel Omni-Path HFI Silicon 100 Series
Switches: Mellanox MSX6036F Infiniband FDR, Qlogic 12300 Infiniband QDR

## Slide 11
Software Stack
Operating System: Linux CentOS 7.4
Fabric Support: Infiniband ver. 13.7, Omni-Path fabric 10.3.1.0-11
GPFS: Spectrum Scale GPFS 4.2.3-2
Services Configuration: RDMA, SRP, Multipath packages, and necessary configurations on NSD servers and storage side
A. Spectrum Scale GPFS Setup
RDMA Service: Provided on both Infiniband and Omni-Path fabrics for GPFS client nodes
Configuration Process:
  Definition of RDMA enabled devices, ports, and subnets for different classes of nodes
  Specific properties assigned to node classes for respective fabrics
  Commands: mmcrnodeclass and mmchconfig verbsPorts used for configuration
Performance: Multifabric layout achieves approximately 1.5 GB/s for IB/QDR client nodes and ~2.5 GB/s for Omni-Path client nodes in I/O transfer rates.

## Slide 12: Conclusion & Acknowledgment:
Conclusion
CRESCO6 in Operation: The successful deployment of CRESCO6 at ENEA's data center.
Multifabric Integration: Integration of diverse fabric technologies (Qlogic/TrueScale, Mellanox, Intel Omni-Path) facilitating high-performance Spectrum Scale GPFS with robust I/O throughput.
Acknowledgment
Acknowledging Resources: Computing resources and technical support provided by CRESCO/ENEAGRID High Performance Computing infrastructure and its dedicated staff [4].